## Slide 1: Testing Supply Substitution Strategies
This resource is intended for labs performing COVID-19 tests that are authorized. This resource includes validated supply alternatives that labs can use to continue performing testing when there is a supply issue with some components of a test.
The information in this resource is not intended to alter any already issued EUA for a COVID-19 diagnostic test nor is it intended to speak to any specific FDA regulatory requirement. Rather, the information is being provided to help address availability concerns regarding certain critical components of COVID-19 diagnostic tests during this pandemic.
START: Go to the Main Menu

## Slide 2
Specimen Collection
Intro to PCR
System Types
PCR Testing Process
Substitution Options
Select a button to learn more about a topic
Learn about specimen collection, swabs, and media
Learn about RT-PCR: what it is and what it’s used for
Compare use of Open Mix and Match Systems vs. Closed Systems, including
instruments, supplies, and reagents
Learn about the steps in the PCR testing process
Learn about substitution options for the Open Mix and Match style CDC test
Real-time RT Polymerase Chain Reaction (PCR) Component Substitution Strategies
Additional Resources
Return to FDA FAQ
Return to the Main Menu

## Slide 3
Explore acceptable choices for swabs
Explore acceptable choices for media
For more information please see the FDA FAQ on this topic under, “What if I Do Not Have…?” It is important that the swab type be appropriate for the anatomic site on which it is used, i.e. only a Nasopharyngeal swab should be used to obtain a Nasopharyngeal specimen.”
Specimen collection is the process of obtaining a sample from a patient, usually by swabbing the nose or mouth, then placing the swab in a tube that is commonly filled with liquid (media) which maintains the sample for transport to the lab.
Originally, specimen collection for SARS-CoV-2 testing required a specialized Nasopharyngeal (NP) swab and Viral Transport Media (VTM)/ Universal Transport Media (UTM).
Options for swabs and media are below.
Specimen Collection
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 4
Return to Specimen Collection
Return to PCR Testing Process
“Collect Specimen from Patient”
Choices for Swabs*
NasoPharyngeal (NP) Swab
OroPharyngeal (OP) Swab
Mid-Turbinate (MT) Swab
Flocked, tapered swab
Anterior Nares (“Nasal”) Swab
Round Foam
Spun Polyester
* For more information please see the FDA FAQ on this topic under, “What if I Do Not Have…?”
It is important that the swab be appropriate for the anatomic site on which it is used, and that the swab type (e.g. polyester vs rayon) is compatible with that platform. Rayon swabs may not be compatible with all molecular testing platforms. Analytical testing should be performed to confirm compatibility with individual platforms.
Specimen Collection: Swabs
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 5
Some transport media may contain guanidine thiocyanate, which produces a dangerous chemical reaction releasing cyanide gas when exposed to bleach (sodium hypochlorite). These media may not be compatible with in vitro diagnostic products that do not utilize guanidine thiocyanate during sample processing.
*WARNING: Do not use PrimeStore MTM with the Hologic Panther or Panther Fusion Systems due to a disinfecting step involving bleach that is specific to the platform. When the bleach interacts with the guanidine thiocyanate in the transport media, it produces dangerous cyanide gas.
Specimen Collection: Media
Choices for Media
VTM/UTM
Liquid Amies-based Media
e.g., Eswab
Nucleic Acid Transport Media
e.g., Primestore MTM*
Saline Solution
Normal saline
Phosphate-buffered saline (PBS)
Additional Resources
Return to the Main Menu
Return to Specimen Collection
Return to PCR Testing Process
“Collect Specimen from Patient”
Return to FDA FAQ

## Slide 6
What Is RT PCR?
RT-PCR stands for “Reverse-transcriptase polymerase chain reaction” (commonly referred to as “PCR”)
RT-PCR is a method used to detect RNA nucleic acids (a type of genetic material)
PCR is used to detect the presence of SARS-CoV-2, the virus that causes COVID-19 disease
Finding SARS-CoV-2 genetic material in a specimen indicates that a person has been infected with the virus
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 7
Open Mix and Match
Amplification
Extraction
Closed System
Extraction and Amplification
Overview of System Types
Additional Resources
Return to the Main Menu
Select a system type for more information
Return to FDA FAQ

## Slide 8
Proprietary Reagent Kit
Extraction and PCR System
Proprietary Reagent Cartridge
Closed System
A single dedicated instrument performs extraction and amplification
Some materials may be specific to the instrument platform
Collection and Media
General Reagents
Supplies and Reagents
Instruments
Additional Resources
Return to the Main Menu
Return to Overview of System Types
Return to FDA FAQ

## Slide 9
Primers and Probes
Extraction System
Instruments
Supplies and Reagents
Master Mix
Collection and Media
General Reagents
PCR System
Open Mix and Match (CDC Design)
Some materials may be usable on more than one system
Extraction and amplification performed separately
Additional Resources
Return to the Main Menu
Return to Overview of System Types
Return to FDA FAQ

## Slide 10: PCR Testing Process
Schematic of SARS-CoV-2 Molecular Diagnostic Assay
Select the STEPs above for more information about the PCR testing process
STEP 1
Collect Specimen from Patient
STEP 2
RNA Nucleic Acid Extraction
STEP 3
RT-PCR Amplification
STEP 4
Results Reporting
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 11
  INPUT FOR THIS STEP? A sample from the patient to test for the presence of SARS-CoV-2
  WHAT SUPPLIES ARE NEEDED?
    A swab to collect the sample.
    Transport Media in a collection tube to transport the sample without degradation. The swab carrying the sample is placed in a collection tube filled with transport media.
  WHAT IS THE OUTCOME? A sample for PCR analysis
Return to PCR Test Process Overview
1. Collect Specimen from Patient
2. RNA Nucleic Acid Extraction
3. RT-PCR Amplification
4. Results Reporting
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 12
  INPUT FOR THIS STEP? A sample for PCR analysis
  WHAT SUPPLIES ARE NEEDED?
    Extraction System
    Extraction Reagents
    Lysis Buffer
    RNA Extraction Control
    Human Specimen Control
    Positive Control specific to SARS-CoV-2
  WHAT IS THE OUTCOME? Extracted nucleic acids
1. Collect Specimen from Patient
2. RNA Nucleic Acid Extraction
4. Results Reporting
3. RT-PCR Amplification
Return to PCR Test Process Overview
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 13
  INPUT FOR THIS STEP? Extracted nucleic acid
  WHAT SUPPLIES ARE NEEDED?
  PCR REAGENTS
    PCR buffer
    dNTPs (building blocks of nucleic acids)
    Reverse Transcriptase (RT)
    No Template Control
    Polymerase (Enzyme)
    Positive Control (specific to SARS-CoV-2)
    Primers and Probe (SARS-CoV-2 specific)
  WHAT IS THE OUTCOME? Fluorescence output signal indicating presence of SARS-CoV-2 RNA
2. RNA Nucleic Acid Extraction
3. RT-PCR Amplification
4. Results Reporting
1. Collect Specimen from Patient
Return to PCR Test Process Overview
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 14
2. RNA Nucleic Acid Extraction
3. RT-PCR Amplification
4. Results Reporting
1. Collect Specimen from Patient
  INPUT FOR THIS STEP? Fluorescence output signal
  WHAT IS THE OUTCOME? Report of output indicating presence of SARS-CoV-2 virus
Return to PCR Test Process Overview
Additional Resources
Return to the Main Menu
Return to FDA FAQ

## Slide 15
Substitution Options*
Select a Test Component on the left to explore possible substitutions for the Open Mix and Match style CDC molecular test
Primers and Probes
SELECT A PCR TEST COMPONENT
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
Additional Resources
Return to the Main Menu
* Substitution Options are illustrated with the CDC test for this tool. Labs can identify and validate alternative options to other authorized assays.
Return to FDA FAQ

## Slide 16
Primers and Probes are the key reagents for direct detection and identification of a given target sequence.
CDC N1
CDC N2
RNaseP
Targets listed in the CDC EUA
BioSearch Technologies
Integrated DNA Technologies
CDC Vetted Acceptable Manufacturers (per CDC guidance)
SELECT A PCR TEST COMPONENT
Additional Resources
Return to the Main Menu
Return to Substitution Options
Primers and Probes
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
Return to FDA FAQ

## Slide 17
  Equivalent Master Mix
The master mix contains the reagents for the PCR process. Alternatives will need to be validated with the PCR system.
Validation Needed
Master mixes listed in the CDC EUA
Quantabio qScript XLT
Quantabio UltraPlex
Promega GoTaq
Thermofisher TaqPath
SELECT A PCR TEST COMPONENT
Additional Resources
Return to the Main Menu
Return to Substitution Options
Primers and Probes
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
Return to FDA FAQ

## Slide 18
The PCR system is the instrument performing amplification.
PCR system listed in the CDC EUA
Applied Biosystems 7500 Fast Dx Real-Time PCR
Applied Biosystems 7500 Fast Real-Time PCR
Applied Biosystems QuantStudio 6 Flex
Applied Biosystems QuantStudio Dx
QIAGEN Rotor-Gene Q MDx
Acceptable Alternatives (per FDA FAQ*)
SELECT A PCR TEST COMPONENT
Additional Resources
Return to the Main Menu
Return to Substitution Options
Primers and Probes
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
* Check FDA FAQ for updates after 6/3/2020
Return to FDA FAQ

## Slide 19
Controls are the reagents that monitor the extraction and amplification process.
Controls listed in the CDC EUA
CDC Positive Control
CDC Extraction Control
BEI Resources (N1, N2 Positive Control)
Integrated DNA Technologies (N1, N2, Rnase P Positive Control)
Human RNA (Rnase P Positive Control, Extraction Control)
Twist Bioscience (Synthetic RNA Controls)
Acceptable Alternatives (per FDA FAQ*)
SELECT A PCR TEST COMPONENT
Additional Resources
Return to the Main Menu
Return to Substitution Options
Primers and Probes
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
* Check FDA FAQ for updates after 6/3/2020
Return to FDA FAQ

## Slide 20
QIAGEN QIAcube/QIAmp DSP Viral RNA Mini Kit
QIAGEN QIAcube/ QIAamp Viral RNA Mini Kit
Roche MagNA Pure LC/Total Nucleic Acid Kit
Roche MagNA Pure Compact/Nucleic Acid Isolation Kit I
Roche MagNA Pure 96/DNA and Viral RNA Small Volume Kit
bioMérieux NucliSENS easyMAG/EasyMAG Extraction Reagents, Biohit Pipette Tips
Beckman RNAdvance Viral XP extraction kit
The Extraction system is the instrument performing extraction. The Extraction kit contains the reagents for the Extraction process.
Extraction Systems/kits listed in the CDC EUA
QIAGEN/QIAmp DSP Viral RNA Mini Kit
QIAGEN/QIAamp Viral RNA Mini Kit
QIAGEN EZ1 Advanced XL/EZ1 DSP Virus Kit, Buffer AVL
QIAGEN EZ1 Advanced XL/EZ1 Virus Mini Kit v2.0, Buffer AVL
Acceptable Alternatives (per FDA FAQ*)
bioMérieux EMAG/EasyMAG Extraction Reagents, EMAG 1000μL Tips
KingFisher Flex/Omega Bio-Tek Mag-Bind Viral DNA/RNA 96 Kit
Applied Biosciences MagMAX Express/Viral/Pathogen Ultra Nucleic Acid Isolation Kit
Promega Maxwell RSC 48/Maxwell RSC Viral Total Nucleic Acid Purification Kit
SELECT A PCR TEST COMPONENT
Additional Resources
Return to the Main Menu
Return to Substitution Options
Primers and Probes
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
* Check FDA FAQ for updates after 6/3/2020
Return to FDA FAQ

## Slide 21
General consumable laboratory supplies used in PCR
General consumables listed in the CDC EUA
Molecular grade water, nuclease-free
Aerosol barrier pipette tips
Microcentrifuge tubes
DNA Decontamination Reagent (DNAZap)
Surface Decontaminant (RNAse Away)
PCR Reaction Plates
Vortex Mixer
Microcentrifuge
Micropipettes
10% Bleach
MicroAmp Optical 8-cap Strips
SELECT A PCR TEST COMPONENT
Additional Resources
Return to the Main Menu
Return to Substitution Options
Primers and Probes
General Consumables
Extraction System/Kits
Controls
PCR System
Master Mix
Return to FDA FAQ

## Slide 22: Additional Resources
FDA Frequently Asked Questions on Diagnostic Testing for SARS-CoV-2
CDC 2019-Novel Coronavirus (2019-nCoV) Real-Time RT-PCR Diagnostic Panel
Return to the Main Menu
Return to FDA FAQ